## Slide 1: Introduction to Signals and Systems
Notes: <number>

## Slide 2: Definitions
<number>
Signal
Conveys information
Function of time
The way it evolves in time is what encodes the information
Examples
  Voltage or current in an electronic circuit
  Speech and music
  Bioelectric signals (e.g. ECG)
Notes: <number>

## Slide 3: Two Types of Signals
<number>
Continuous-time signals
Discrete-time signals
Notes: <number>

## Slide 4: 1. Continuous-Time Signals
<number>
Signal that has a value for all points in time
Function of time
  Written as x(t) because the signal “x” is a function of time
Commonly found in the physical world
  ex. Human speech
Displayed graphically as a line
Notes: <number>

## Slide 5: 2. Discrete-Time Signals
<number>
Signal that has a value for only specific points in time
Typically formed by “sampling” a continuous-time signal
  Taking the value of the original waveform at specific intervals in time
Function of the sample value, n
  Write as x[n]
  Often called a sequence
Commonly found in the digital world
  ex. wav file or mp3
Displayed graphically as individual values
  Called a “stem” plot
Sample number
Notes: <number>

## Slide 6: Discrete-Time ≠ Digital
<number>
Discrete-time sequences are continuous in values, but discrete only in time
Digital signals are discrete in values and discrete in time (they can only take on specific values)
Notes: <number>

## Slide 7: Systems
<number>
System
A collection of items that together performs a function
Modifies / transforms an input to give an output
Represented by
System
T{ }
x(t)
y(t) = T{x(t)}
T = input2
x(t)
y(t) = T{x(t)} = x2(t)
ex. A squaring system
Notes: <number>

## Slide 8: System Examples
<number>
Real-World Examples of Systems
Circuits
Car
  Inputs  Steering wheel, force on accelerometer and brakes
  Outputs  Position of car, velocity
Chemical processes
Electromechanical systems (motors)
Economics, stock market
Biological processes (heart)
Notes: <number>

## Slide 9: Two Types of Systems
<number>
Continuous-time systems
  Operate on continuous-time signals
  Commonly found in the physical world
  Represented mathematically using differential equations
  System parameters are defined on a continuum of time
Discrete-time systems
  Operate on discrete-time signals
  ex. Computer algorithms
  Represented mathematically by difference equations
  System parameters are defined only at discrete points in time
Notes: <number>

## Slide 10: Hybrid Systems
<number>
Most real systems are hybrid systems
  Use both CT and DT systems
ex. Audio delay system
CT
System
ADC
DT
System
DAC
CT
System
a(t)
b(t)
c[n]
d[n]
e(t)
f(t)
Amplification
Analog-to-Digital converter
Sampler
CT to DT
ex. Delay
Digital-to-Analog converter
DT to CT
ex. Smoothing filter
Notes: <number>

## Slide 11: Audio Delay System Example
<number>
CT
System
ADC
DT
System
DAC
CT
System
a(t)
b(t)
c[n]
d[n]
e(t)
f(t)
Amplification
Analog-to-Digital converter
Sampler
CT to DT
ex. Delay
Digital-to-Analog converter
DT to CT
ex. Smoothing filter
Sample at a constant rate (time period)
Notes: <number>

## Slide 12: Creating Useable Systems
<number>
Purpose of system design
  To create an I/O relationship that is predictable
The system I/O relationship must be the same every time … the same today as it was yesterday and will be tomorrow
  Time Invariant
Given any type of input, the output follows a reasonable relationship
  Easiest is Linear
Linear
Nonlinear
Notes: <number>

## Slide 13: LTI System
<number>
Most engineering systems are designed to be linear and time invariant (LTI) so that they are predictable
The rest of this course focuses on LTI systems
  How to analyze
  How to use
  How to design
Notes: <number>